## Slide 1
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · DETAILED SITE ZONING
SURVEY READING — LEVELS
Contours from the survey (+4' … +28'), grouped into four bands. Everything below is measured off the drawing.
01
A
A'
ENTRANCE ±0'
NE bank: +4' at the boundary
old Press Club (to be removed)
existing stairs
existing summit structures
FOUR BANDS (ground area inside the traced site edge)
0' → +4' base ≈31,700 sq ft — flattest: NW pocket, S edge, old Press Club site
+4' → +12' lower slope ≈35,800 sq ft — gentle on the S, a steep bank on the NE
+12' → +28' flanks ≈17,200 sq ft — contours 4' apart at ~10–15' spacing: steep
+28' summit ≈20,000 sq ft — a broad plateau with existing structures
WHAT THIS MEANS FOR ZONING
Build low most built program on the 0'–4' base and the gentle S slope — no cutting.
Keep the flanks the +12'–+28' band is too steep to build on without regrading.
Open the top the summit is already a public place — keep it open.
NE edge the ground reaches +4' at the boundary: only a thin bar, stepping.
0'–4' base (white = below +4')
+12'–+28' flanks
+28' summit
old Press Club outline (removed)
Traced site edge ≈ 105k sq ft (inner boundary line). Handout: 136,530 sq ft, probably to the outer line. Scale read from dimension strings (≈2.68 px/ft at 2000 px width).

## Slide 2
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · DETAILED SITE ZONING
DETAILED PROGRAM ZONING
Every program group placed on the band that can take it. Figures = ground available in each zone (not building area).
02
PRINT · DISPATCH
≈2,900 sq ft ground
ARCHIVE
≈2,700 sq ft ground
RESEARCH
≈1,100 sq ft ground
MEDIA · EDITORIAL
≈3,800 sq ft ground
WORKSHOPS
≈1,800 sq ft ground
ADMIN
≈2,100 sq ft ground
ENTRY FORUM
≈3,400 sq ft ground
EXHIBITION · PRESS CONF.
≈6,000 sq ft ground
AUDITORIUM
≈6,400 sq ft ground
LIBRARY + READING
≈5,400 sq ft ground
OPEN FORUM (summit)
≈20,000 sq ft ground
SLOPES
≈17,200 sq ft ground
NEW PRESS CLUB
≈5,900 sq ft ground
GAMES + RECREATION
≈5,000 sq ft ground
CAFE · BOOKSHOP
≈5,400 sq ft ground
GAMES COURT
≈3,300 sq ft ground
public / civic
knowledge
media / production
archive (protected)
learning
admin / service
press club / games
landscape / slopes
open summit
old Press Club (removed)
PLACEMENT LOGIC
S base (0'–4') entry forum at the survey's ENTRANCE; exhibition + press conference along Davis Rd S.
S slope (+4'–+12') auditorium raked on the SW slope; library + reading on the existing stair route.
NW pocket (+1') print + dispatch with a service yard — the only flat ground away from the entrance.
NE bank archive + research at the NW end, media + editorial at the SE end, next to the new press club.
Old Press Club site (+1'–+8') removed; its flat ground takes a new press club (lounge, dining, meeting), games + recreation, a cafe + bookshop on the forum and an outdoor games court.
E edge workshops next to media; admin + staff entry on the E side.
Flanks + summit no new building: landscape, existing stairs, open forum at +28'.
Existing Press Club removed (my design decision; handout asks to re-envision the existing built environment). Dashed = its old outline, approximated from the survey. NW existing structure kept — use to be decided.

## Slide 3
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · DETAILED SITE ZONING
ACCESS + CIRCULATION
Public enters at the surveyed ENTRANCE (+0'); service and staff kept off the public route.
03
PRINT · DISPATCH
ARCHIVE
RESEARCH
MEDIA · EDITORIAL
WORKSHOPS
ADMIN
ENTRY FORUM
EXHIBITION · PRESS CONF.
AUDITORIUM
LIBRARY + READING
OPEN FORUM (summit)
SLOPES
NEW PRESS CLUB
GAMES + RECREATION
CAFE · BOOKSHOP
GAMES COURT
public — entrance → forum → stairs → summit
staff · journalists — E edge → NE bars
service — Davis Rd (N end), proposed
ROUTES
Public entrance → entry forum → exhibition foyer → existing S stairs → library → summit. Branches to the auditorium and the W stairs.
Staff + journalists from the entrance along the E edge → admin → press club → media → research → archive.
New press club journalists move N into media; the club, cafe and games open onto the forum.
Service one yard at the NW pocket (+1'); vehicles never enter the S forum. Access point is proposed — not on the survey.
CONFLICTS AVOIDED
Forum staff route peels off E before the crowd.
Summit public only; working bars sit below it on the NE bank.

## Slide 4
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · DETAILED SITE ZONING
SECTION A–A' · ENTRANCE SIDE → SUMMIT → DAVIS ROAD N
Profile read from the survey contours along line A–A' (slide 01). Vertical scale ×3.
04
+0'
+4'
+8'
+12'
+16'
+20'
+24'
+28'
EXHIBITION · PRESS CONF.
LIBRARY + READING
OPEN FORUM
ARCHIVE
ENTRANCE SIDE (S)
DAVIS ROAD (N)
steep flank — landscape + existing stairs
public route
READING THE SECTION
Built program sits where the ground is low or gentle (left: exhibition, library; right: archive on the NE bank). The steep flanks stay landscape; the summit plateau stays an open public forum. Floors step with the ground on piers; nothing is cut or filled.

## Slide 5
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · DETAILED SITE ZONING
PROGRAM PLACEMENT SCHEDULE
Where every program item goes, on which level, and why. Areas are ground available — building areas still to be set.
05
PROGRAM ITEM | ZONE | LEVEL | ACCESS | WHY HERE
Entry forum · arrival · protest edge | S base, at ENTRANCE | ±0' – +1' | public | the survey's only marked entrance; Davis Rd S frontage
Exhibition · press conference · forum hall · foyer | S base / lower slope, W of the cafe | +1' – +8' | public | faces the forum and Davis Rd S
Auditorium | SW slope | +4' – +12' | semi-public | rake follows the existing slope; foyer at the low end
Public library + reading room | S slope on the existing stairs | +4' – +12' | semi-public | on the public route up; reading terrace faces the summit
Open forum · viewing | summit plateau | +28' | public | already a public top with structures; nothing new built
Archive stores · conservation · consultation | NE bank, NW end | +1' – +12' | private / controlled | beside the service yard; away from the crowd
Research studios · seminar | NE bank, next to archive | +4' – +12' | semi-private | research ↔ archive
Media: newsroom · editorial · recording · broadcast · editing | NE bank, SE end | +4' – +12' | working | next to the new press club (journalists)
Print · paper store · dispatch · service yard | NW pocket | +1' | private | only flat ground away from the public entrance
Workshops · education | N of the new press club | +4' – +12' | semi-public | between media (skills) and the public side
Admin · staff entry · security | E edge | +1' – +4' | private | on the staff route, close to the entrance
Slopes (+12' – +28') | flanks | — | public landscape | too steep to build without regrading
New press club: members' lounge · dining · meeting rooms | old Press Club site, N part | +4' – +8' | members / semi-private | journalists' home next to media; replaces the removed club
Games + recreation: snooker · table tennis · carrom · chess | old Press Club site, E part | +1' – +4' | semi-public | flat ground; shared by members + public
Cafe · canteen · bookshop | old Press Club site, S part | +1' – +4' | public | opens straight onto the entry forum
Outdoor games court | SE corner | +1' | public | flat corner by the entrance; overflow for events