## Slide 1
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
SITE ANALYSIS
Base: the site plan provided in the project handout (p.4), unaltered, shown in light grey. Highlights are overlays.
01
NW JUNCTION
SE JUNCTION
LEAST TREE COVER (as drawn)
DENSE TREES (as drawn)
DAVIS RD · media street (handout)
SE EDGE → Davis / Durand
SHIMLA PAHARI · contoured (plan note) · levels not shown
IDENTIFIED ON THE PLAN
Boundary ≈136,530 sq ft · 3.134 ac, oval island
Roads Empress · Egerton · Abbot (NW) · Davis · Durand (SE)
Junctions two, one at each tip, with traffic islands
Trees dense at W end + perimeter; least cover centre-east
NOT IDENTIFIABLE FROM PROVIDED SITE PLAN
Press Club no footprint or entrances drawn
Contours site noted as contoured, no levels
Existing access no gates / paths drawn
North · scale not shown
Views · noise · protest spot not shown
Names of the two long-side roads not labelled
FROM THE HANDOUT (TEXT)
Davis Rd historically a media street
Mound artificial, brick-kiln origin
Rule topography not to be altered
site boundary
SE public edge / Davis Rd
dense trees (as drawn)
least tree cover (as drawn)
road junction

## Slide 2
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
OPPORTUNITIES + CONSTRAINTS
What the drawn site offers, and what limits it.
02
1
2
3
4
A
B
C
D
OPPORTUNITIES
1 SE tip faces the Davis / Durand junction: the handout's media street — the public, civic end.
2 Centre-east has the least tree cover as drawn: the most buildable ground.
3 Dense W-end trees: keep as a landscape the public can walk through.
4 NE long edge has a thin stretch of trees: possible service entry.
CONSTRAINTS
A Topography must not be altered — levels unknown: building placement to be checked against a survey.
B Tree ring along almost the whole perimeter: entries must thread between trees.
C Roads on every side: all edges exposed to traffic (volumes not shown).
D Press Club position unknown: zoning must stay flexible around it.
opportunity (numbered)
constraint (lettered)

## Slide 3
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
PUBLIC / PRIVATE ZONING
Not a straight line: public at the SE edge AND an open top; working parts split to face the service edge.
03
PUBLIC
SEMI-PUBLIC
SEMI-PRIVATE
PRIVATE
PUBLIC LANDSCAPE
PUBLIC TOP
city arrives here
service edge → private side
WHY EACH SITS WHERE IT DOES
Public the SE tip meets the junction and the media street — where crowds, cameras and speech already arrive.
Semi-public next ring in: reached through the public zone, never directly from the road.
Semi-private SW side of the centre, away from the service edge: research + archive reading.
Private NE side of the centre, next to the only thin tree stretch: loading reaches it without crossing public ground.
Public landscape + top the wooded W end and the open top stay public: the gradient reverses as you reach them.
public
semi-public
semi-private
private
public landscape (preserved)
Gradient is my design interpretation; zone lines are diagrammatic, to be checked against levels + Press Club position.

## Slide 4
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
PROGRAM ZONING
Large program clusters on the site — no rooms, no areas yet.
04
G FORUM UNDER TREES · PROTEST EDGE
A EXHIBITION · FORUM · AUDITORIUM · PRESS
B LIBRARY + READING
C/D MEDIA · EDITORIAL · PUBLISHING
F ADMIN · SERVICE
E WORKSHOPS · EDUCATION
B ARCHIVE + RESEARCH
H PRESERVED LANDSCAPE
OPEN TOP
A · G PUBLIC / CIVIC — forum, auditorium, exhibition, gathering
B KNOWLEDGE — library, reading, archive, research
C/D PRODUCTION — editorial, publishing, media
E LEARNING — workshops, education
F ADMIN / SERVICE
H LANDSCAPE — preserved, walkable
READING ORDER (SE → NW)
1 road + junction → forum under trees (G)
2 civic halls facing it (A)
3 library + learning, side by side (B, E)
4 archive + research | media + publishing (B, C/D)
5 open top → wooded W end (H)
WHY THIS ORDER
Public program sits where the public already arrives; knowledge sits between the public and production so both reach it; production sits on the service edge; the most wooded ground stays unbuilt.
Program from handout: required = library + reading, archive, research + studios, media + recording, publishing. ‘May include’ = exhibition, forum, auditorium, workshops, education.

## Slide 5
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
ACCESS + USER CIRCULATION
Three separate systems. Entry points are PROPOSED — existing gates are not shown on the plan.
05
!
crowd vs staff arrival
!
service vs pedestrians
!
public route vs research
PUBLIC ARRIVAL
SERVICE ENTRY (proposed)
GENERAL PUBLIC — junction → forum → halls → library → open top
JOURNALISTS · RESEARCHERS · STAFF — own entry + route
SERVICE / DELIVERY — NE edge only
public path through the wooded W end
CONFLICT POINTS → ZONING ANSWER
SE tip protest crowds + staff arriving together → staff get a second door off the SE route, beside the press room, not through the forum.
NE edge delivery vehicles cross the footpath → one short service bay only, next to production, trees kept either side.
Centre public route passes research → research on the SW side, route on the NE of it; windows, not doors, face the path.
RESTRICTED
archive stores · production floor · loading · admin

## Slide 6
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
THREE ZONING OPTIONS
Same site, same program, three priorities. Not ranked.
06
A PUBLIC-CENTRIC
A public street crosses the whole site, junction to junction; civic halls at both ends.
+ strongest public presence; links both junctions · − cuts the wooded W end; production split by the street; many entries to secure
B KNOWLEDGE / PRODUCTION
One compact knowledge + production core on the least-wooded ground; small public front at the SE tip.
+ efficient, easy to service and secure; smallest disturbance · − public limited to one edge; weakest civic engagement
C SITE / TOPOGRAPHY
Rings follow the mound: public along the toe, knowledge mid-slope, open top; W end kept.
+ reads the mound; open top; route climbs · − depends on real levels (not on plan); ring along the toe faces traffic
PRESS CLUB shares the SE civic end, or sits on the street
ROAD both junctions open
TOPOGRAPHY street must cross levels
PRESS CLUB stands as the core's public face
ROAD one public edge (SE)
TOPOGRAPHY built area smallest
PRESS CLUB joins the outer public ring
ROAD whole toe faces the road
TOPOGRAPHY zoning follows levels
public / civic
knowledge
production
landscape

## Slide 7
SITES OF REPRESENTATION · THE CONTEMPORARY PUBLISHING HOUSE · SITE ZONING
FINAL ZONING
Draws on all three: B's compact core, C's reading of the mound, A's public arrival.
07
G FORUM UNDER TREES · PROTEST EDGE
A EXHIBITION · FORUM · AUDITORIUM · PRESS
B LIBRARY + READING
C/D MEDIA · EDITORIAL · PUBLISHING
F ADMIN · SERVICE
E WORKSHOPS · EDUCATION
B ARCHIVE + RESEARCH
H PRESERVED LANDSCAPE
OPEN TOP
WHY IT WORKS
SITE public where the junction and media street are; building on the least-wooded ground; the W woods stay.
PROGRAM knowledge in the middle, reachable from both the public and the working side.
USERS three separate entries; they meet in the forum, library and on the route.
VISION the public reaches the top of the landmark; production is next to the route, not hidden.
TOPOGRAPHY zones follow the mound in plan; no flattening. Levels to be surveyed.
PRESS CLUB OPTIONS (not on plan)
If near the SE tip keep it; it becomes the press face of the civic zone A, sharing the forum G.
If mid-site keep it; the public route passes it; link at ground level.
If in the W woods keep it as a pavilion in the landscape; connect by path.
public / civic
knowledge
production
learning
landscape
public
staff
service

## Slide 8
ZONING BOARD (A1 landscape, scaled)
SITE ZONING — SHIMLA PAHARI
SITE → CONDITIONS → OPPORTUNITIES / CONSTRAINTS → ACCESS → USERS → PROGRAM → OPTIONS → FINAL
01 SITE CONDITIONS
02 PUBLIC / PRIVATE
03 ACCESS + USERS
04 OPTION A
05 OPTION B
06 OPTION C
07 FINAL ZONING
public / civic
knowledge
production
learning
landscape
public
staff
service
Public where the city arrives · knowledge in the middle · production on the service edge · woods and top stay open.
Base: handout site plan (p.4). Press Club footprint, levels and existing gates are not shown on it and must be added from a survey.